## Slide 1: Weekly Meeting
29nd January, 2021

## Slide 2: Outline
Measuring performance of Random Number Generator (RNG)
Measuring performance before and after cache warmup

## Slide 3: Time Consumption in RNG
Community Optimization Time (sec) | RNG Generation Time (sec) | Number of Random Number generated | RNG Generation Time (%)
183.92 | 0.88 | 4251134 | 0.48
186.45 | 0.90 | 4351167 | 0.48
186.11 | 0.89 | 4326486 | 0.48
Note: The experiments are executed in 4 compute nodes, dataset used Youtube network

## Slide 4: Pre-Warmup and Post-Warmup comparison (Last Week RECAP)
Network Name | Million Link Processed/second (PreWarmup) | Million Link Processed/second (PostWarmup) | % Increase
DBLP | 3.36 | 3.57 | 6.25
Youtube | 3.66 | 3.87 | 5.73
Pokec | 4.26 | 4.42 | 3.75
Libjournal | 4.07 | 4.25 | 4.4
Orkut | 4.36 | 4.53 | 3.4

## Slide 5: Cache Hit Rate (Pre-Warmup and Fixed Iteration)
Note: The traversal loop was executed 32768 times. Given each map access is 12 bytes, the total size of the memory access is 32768*12 = 384 KB. L2 cache size is 512 KB, therefore all the map access data should fit into L2 cache

## Slide 6: Cache Hit Rate (Post-Warmup and Fixed Iteration)
Note: The traversal loop was executed 32768 times. Given each map access is 12 bytes, the total size of the memory access is 32768*12 = 384 KB. L2 cache size is 512 KB, therefore all the map access data should fit into L2 cache

## Slide 7: Cache Hit Rate (Pre-Warmup and Random Iteration)

## Slide 8: Cache Hit Rate (Post-Warmup and Random Iteration)

## Slide 9: Information on MAP time
Community Optimization (sec) | Map Operation Time (sec) | >= Percentage (%)
183.73 | 103.86 | 56
206.63 | 113.79 | 55

## Slide 10: Appendix

## Slide 11: Sample Code Snippet for Map Operation
flowmap outFlowToMod; // <modId, flow> for outFlow...
flowmap inFlowFromMod; // <modId, flow> for inFlow...
//mark 2_2 subbegin
double mark_22 = MPI_Wtime();
for (link_iterator linkIt = nd.outLinks.begin();
linkIt != nd.outLinks.end(); linkIt++) {
int newMod = nodes[linkIt->first].ModIdx();
if (outFlowToMod.count(newMod) > 0) {
outFlowToMod[newMod] += beta * linkIt->second;
} else {
outFlowToMod[newMod] = beta * linkIt->second; // initialization of the outFlow of the current newMod.
inFlowFromMod[newMod] = 0.0;
nModLinks++;
}
}

## Slide 12: Assumption for theoretical Peak (KNL)
Infinite L2 memory with latency (~ 115 cycles)
Infinite MCDRAM memory with latency (~ 185 cycles)
No L1 cache, only L2 or lower level cache/memory exist
Notes: 1. https://stackoverflow.com/questions/21369381/measuring-cache-latencies

## Slide 13: Computation for theoretical Peak (L2)
The Intel Xeon Phi core has 64 bytes/cycle L2 bandwidth [5]. Therefore,
1 floating point operation ~ 1 cache block (64 bytes) access/read operation
So, 115 cycles ~ 1 operation (query) /sec [2]
For an instantiation of Intel® Xeon Phi™ coprocessor single core, running at 1.4 GHz [2]
Megabytes/sec = × 10^3 = 779.13
Notes: 2. https://software.intel.com/content/www/us/en/develop/articles/intel-xeon-phi-core-micro-architecture.html#:~:text=The%20Intel%20Xeon%20Phi%20core,64%2Dbit%20integer%20vector%20instructions.
5. https://www.nersc.gov/assets/Uploads/Using-KNL-Processors-Feb2019.pdf

## Slide 14: Computation for theoretical Peak (MCDRAM)
The Intel Xeon Phi core has 64 bytes/cycle L2 bandwidth [5]. Therefore,
1 floating point operation ~ 1 cache block (64 bytes) access/read operation
So, 185 cycles ~ 1 operation (query) /sec [2]
For an instantiation of Intel® Xeon Phi™ coprocessor single core, running at 1.4 GHz [2]
Megabytes/sec = × 10^3 = 484.32
Notes: 2. https://software.intel.com/content/www/us/en/develop/articles/intel-xeon-phi-core-micro-architecture.html#:~:text=The%20Intel%20Xeon%20Phi%20core,64%2Dbit%20integer%20vector%20instructions.

## Slide 15: Rb Tree Access (map in c++) Before Cash Warmup
Time = 80.67 sec, total object (link) accesses = 351602917
Accesses per second = 351602917/80.67 = 4358533
Each link object 12 bytes
Therefore, Bytes accessed/read per second = 4358533 *12 = 52302396
I.e. 52302396 /10^6 = 52.30 MB/sec

## Slide 16: Rb Tree Access (map in c++) After Cash Warmup
Time = 77.62 sec, total object (link) accesses = 351602917
Accesses per second = 351602917/77.62 = 4529797
Each link object 12 bytes
Therefore, Bytes accessed/read per second = 4529797 *12 = 54357564
I.e. 54357564 /10^6 = 54.36 MB/sec